Lavice REWIND RW 1120-1320, RW 1130-1330, RW 1140-1340

SITTY SI 6620 A

Manufacturer: RIM CZ a.s.

SITTY SI 6520 A (bench)

Two seater bench suitable for public areas with a modern, light design. The shell firmly attached to the metal frame.

| Seat + backrest | The bent pressed beech shell is firmly fixed to the metal frame. The strength of the shell attachment allows even for very strenuous use. The total number of veneers is 11. Individual veneer layers are 1.2 mm thick. |
| --- | --- |
| Upholstery | A thin panel screwed to the front part of lacquered shell, with 10 mm PUR foam thickness. |
| Fabric | To be selected from fabric collection. |
| Frame | The frame consists of metal girder with rectangular cross-section of 40x80x2 mm with attached surface for shells and legs from a bent profile with plastics glides. Girder surface treatment – durable powder coating as per RAL 9011. |
| Options | Colour shell treatment – white or black laminate. Chrome legs |
| Warranty | 5 years (see Business conditions). |

Dimensions (in mm)

Variants

| SI 6420 A | 2-seater bench. The shaped shell is without upholstery and lacquered with natural, water dissolvable lacquer. |
| --- | --- |
| SI 6520 A | 2-seater bench. The shaped shell with thin panel screwed to the lacquered shell on the sitting part. |
| SI 6620 A | 2-seater bench. The shaped shell is upholstered with PUR foam to a thickness of 10 mm and coated with fabric. |
| SI 6430 A | 3-seater bench. The shaped shell is without upholstery, lacquered with natural, water dissolvable lacquer. |
| SI 6530 A | 3-seater bench. The shaped shell with thin panel screwed to the lacquered shell on the sitting part. |
| SI 6630 A | 3-seater bench. The shaped shell is upholstered with PUR foam to a thickness of 10 mm and coated with fabric. |
| SI 6440 A | 4-seater bench. The shaped shell is without upholstery and lacquered with natural, water dissolvable lacquer. |
| SI 6540 A | 4-seater bench. The shaped shell with thin panel screwed to the lacquered shell on the sitting part. |
| SI 6640 A | 4-seater bench. The shaped shell is upholstered with PUR foam to a thickness of 10 mm and coated with fabric. |

SI 6430 A, SI 6530 A, SI 6630 A

SI 6440 A, SI 6540 A, SI 6640 A